IOS Command/Syntax/Mode	Purpose	Notes
“User Mode”	For basic monitoring of a router or switch	Very limited range of permitted commands. Some of the show commands can be used in this mode such as “show ip route” to see the current routing table.
“Privileged Mode”	For advanced monitoring of a router or switch-often locked with a password due to it’s critical nature.	The whole device is accessible from this mode-all the show and debug commands as well as commands for erasing and reloading the device. On switches, the VLAN databases van be adjusted from here or deleted.
“Global Configuration Mode”	Used for all configuration commands	Configuration of device interfaces and protocols is achieved in this mode. Note: show commands are not active in this mode.
exit	Switch to previous device mode	E.g. moving back from Global Configuration Mode to Privileged Mode.
Hostname	Used to give routers specific names.	Used in global configuration mode.
Show	Used for diagnosis	Used in privileged mode
Configure Terminal	Command used to enter global configuration mode	Used in privileged mode. / Used as conf t” in short.
Ipv6 unicast-routing	Used to enable Ipv6-routing.	Used in config mode
Interface port	Used to specify the interface to be addressed	“int” in short.
No shutdown	Used to turn an interface on	No shut is it’s short form
Ip version rip(name) enable	To start up a routing protocol
Clock rate	To assign clock rate to a router
Write memory	Used to save configuration to the router.	Short form (wr)
Ping	Network testing device used to check device connection
Tracert	Tells you the whole journey across a network	Short form (trace)
no	When inserted in front of ant command, it removes the command.	e.g no ipv6 rip mynet enable : Used remove rip from routers when configuring static and default routes.
Ipv6 route <network/subnet> <next-hop>	Used to configure static routes.	e.g. ipv6 route fc00::/64 2001::1 – this would add a static route to the network fc00::/64 via the interface 2001::1 on the adjoining router
Ipv6 router rip <name>	To enter router config mode
Redistribute static	Enables communication between devices in a network.	Typed once in router config mode.
Show ipv6 route	Used to show the ipv6 routing table of a router.
Show running config	To display the configuration information currently running.	Short form (show run)
Ipv6 enable	This enables the use of SLAAC	Used in global config mode.
Default-information originate	Configures ospf to advertise the default route (0.0.0.0/0) to it’s neighbors regardless if it is present in the routing table.	Used in global config mode.